## Slide 1: NAVOLCHI meeting Warwick, July 2012 Victor Dolores-Calzadilla Andrea Fiore Meint Smit

## Slide 2: Outline
Roadmap: milestones and deliverables
Progress:
    Fabry Perot plasmonic laser
    Metallo-dielectric nanolaser
Conclusions

## Slide 3: Work package no. 3
Task 3.1 - Modeling of device structures plasmonic laser and optimization of bonding technology [M1-M6]
  The aim of this task is to look at the choice of laser design and how to couple the laser output to the Si waveguide.
  Task leader: TUe
  Contributing Partners: TUe, IMEC
Task 3.3 - Fabrication of nano plasmonic laser [M7-M30]
  The fabrication of the nanolaser will be done by epitaxial grown InP/InGaAs wafer, bonding it to the SOI waveguide structure, and then performing lithography, etch and material deposition steps to form the laser.
  Task leader: TUe
  Contributing Partners: TUe, IMEC

## Slide 4: Deliverables and milestones
Deliverables
M8 - 04/2012 – Optimization of metallic/plasmonic nanolaser and its coupling to Si waveguides
M13 - 04/2013 - Initial characterization of unbonded plasmonic lasers
M15 - 10/2013 - Initial testing of bonded plasmonic lasers
Milestones
D3.1 - 10/2012 - Report on the studies of optimized structure for metallic/plasmonic nanolaser and its coupling to Si waveguides
D3.3 - 10/2013 - Fabrication of plasmonic laser device
D6.1 – 01/2014 – Input to report on characterization results of all plasmonic devices (ST?)
D7.1/D7.3 - 10/2012 – Dissemination and promotion activities
3 years period (started on 01/11/2011)
?
?
D6.1 (ST) D7.3 (AIT)
M47 (AIT)

## Slide 5: Fabry Perot plasmonic laser
FP cavity
Output waveguide

## Slide 6: Mode properties: propagation loss
The width w has an influence on the confinement and propagation loss
The post height h determines the facet reflectivity and outcoupling
When the post height increases the propagation loss decreases

## Slide 7: Mode properties: confinement factor
(a)
(b)
Decreasing the thickness of the insulation layer leads to a better confinement, however the propagation loss is also increased
The confinement factor increases for wider structures, however additional low loss (dielectric) modes could exist for very wide structures.

## Slide 8: Facet reflectivity
Reflectivity increases for a higher post height
The reflectivity achieved is twice the Fresnel reflection for an interface of InGaAs-air considering perpendicular incidence.
A full metal termination provides

## Slide 9: Coupling to waveguide
The outcoupling decreases for a higher post height, since the vertical distance between the plasmonic mode and the dielectric waveguide is increased

## Slide 10: Threshold gain and external efficiency
Considering ,
For example:
  If 𝐿 = 50 𝜇m
  →
  If 𝐿 = 10 𝜇m
  →

## Slide 11: Metallo-dielectric nanolaser
Wide active core
Undercut
Thick insulation
layer
Symmetric cavity:
Length and width are initially the same

## Slide 12: Q factor and external efficiency
,
,
𝑝𝑜𝑠𝑡 ℎ𝑒𝑖𝑔ℎ𝑡𝑛𝑚
For a thin insulation  high absorption
For a thick insulation  high outcoupling loss
Q-factor decreases for a short post leading to an increase of external efficiency

## Slide 13: Efficiencies and threshold gain
The confinement factor decreases when increasing the length, however it keeps around
Post height = 250 nm
Insulation thickness = 100 nm
Post height = 250 nm
Insulation thickness = 100 nm

## Slide 14: Comparison
Metallo-dielectric laser
  (both directions)
  Length
  Active region:
Metallo-dielectric laser has:
  ~ 5 times lower threshold gain
  ~ 20 times higher current density for the same pumping current.
FP plasmonic laser
  Length = 14 𝜇𝑚
  Active region:

## Slide 15: Conclusions
Room temperature operation of a FP plasmonic laser longer than 50 𝜇𝑚 is possible only at high current densities and low efficiency.
High Q-factor Metallo-dielectric lasers supporting a dielectric mode offer much better performance.
We will fabricate a metallo-dielectric nanolaser on a III-V wafer bonded to silicon. For simplicity, we will firstly demonstrate a device operating with an InP output waveguide.

## Slide 16
Questions ?