## Slide 1
Work Package 3: Plasmonic Transmitter
Victor Dolores-Calzadilla, Meint Smit
Eindhoven University of Technology (TU/e), The Netherlands

## Slide 2: Outline
WP3 Position in Project
Objectives
Tasks
Milestones and Deliverables
Status of Work
  Plasmonic/Metallic Laser
  Plasmonic Modulator
Summary and Outlook

## Slide 3: WP3 Position in Project
Contributors:

## Slide 4: Objectives
Simulation studies
  Plasmonic/metallic nanolaser
  Plasmonic modulator
Fabrication
  Electrically pumped plasmonic/metallic nanolaser
  Electrically driven plasmonic modulator
Performance targets
  Laser: active region < 1 mm2, output power > 100 mW
  Modulator: extinction ratio > 3dB for length < 10 mm, and a total modulation speed > 40 Gbit/s

## Slide 5: Tasks
 | Names of the Tasks | Time Period [months]
Task 3.1 | Modelling of plasmonic laser and optimization of bonding technology | 1 – 6
Task 3.2 | Modelling of plasmonic modulator | 1 – 18
Task 3.3 | Fabrication of plasmonic/metallic nanolaser | 7 – 30
Task 3.4 | Fabrication of Si-plasmonic modulators | 7 – 27

## Slide 6: Milestones
 | Names of the Milestones | Month | Partner
MS8 | Decision on an optimized structure for metallic/plasmonic nanolaser and its coupling to a Si-waveguide | 6 | TU/e
MS9 | Decision on an optimized structure for plasmonic modulator | 6 | KIT
MS10 | Grown wafer structure for plasmonic lasers | 12 | TU/e
MS11 | Fabrication of plasmonic modulator on a SOI platform | 15 | KIT
MS12 | Decision on an optimized structure for plasmonic modulator with a maximum loss of 20dB | 18 | KIT
MS13 | Characterization of initial fabrication results of plasmonic/metallic lasers | 18 | TU/e
MS14 | Initial testing and characterization of plasmonic modulators | 21 | KIT
MS15 | Initial testing of bonded plasmonic lasers | 24 | TU/e

## Slide 7: Deliverables
 | Names of the Deliverables | Month | Partner
D3.1 | Report on studies of optimized structure for metallic/plasmonic nanolaser and its coupling to Si-waveguide | 12 | TU/e
D3.2 | Report on modelling of the modulator structure | 12 | KIT
D3.3 | Fabrication of plasmonic laser device | 24 | TU/e
D3.4 | Report on fabrication of modulators | 24 | KIT

## Slide 8: Metallic/Plasmonic Laser Approaches
Fabry-Perot plasmonic laser
Metallo-dielectric nanolaser
  High propagation loss ( ~ 0.16 dB / µm)
  Poor confinement in active region
Reported in MS8 & D3.1
xy
V. Calzadilla et al., Towards plasmonic lasers for optical interconnects, ICTON, 2012
V. Calzadilla et al., Waveguide-coupler nanolasers in III-V membranes on silicon , ICTON, 2013
|E|2
|E|2

## Slide 9
Optical and electrical optimization of metallo-dielectric nanolaser
Q ~ 530 @ 1.55 µm
Threshold gain ~ 800 cm-1
Threshold current ~ 120 µA
Differential efficiency ~ 0.16
Output power ~ 40 µW @ 420 µA (2V)
Evanescent coupling, log(|E|2)
Task 3.1 Modelling of the Nanolaser
Dimensions:
  Pillar: 300nm x 400nm x 1µm (height)
  Waveguide: 400nm x 250 nm

## Slide 10
Task 3.1 Modelling of the Nanolaser
Thermal simulations
Self-heating  Footprint vs Output power
(no self-heating)
7 mW/mm2K
Heat sink/spreading layer
Planarization layer
Ag
p
n

## Slide 11
Water cooled:
95 mW/mm2K [2]
Fan cooled:
7 mW/mm2K [1]
[1] Guenin B., Electronics Cooling, Vol. 16, No. 12, (2010)
[2] Colgan E.G. et al. , IEEE Transactions on components and packaging technologies, Vol. 30, No. 2, (2007)
Task 3.1 Modelling of the Nanolaser
Periodic report (M1-M18)
Output power and integration density

## Slide 12
EBL + development
Polymer RIE
Nitride RIE
ICP-RIE
EBL + development
ICP-RIE
No sidewall roughness
High verticality is possible
Nanopillars
Waveguides
Task 3.3 Fabrication of the Nanolaser
Periodic report (M1-M18)

## Slide 13: Task 3.3 Fabrication of the Nanolaser
Tests carried out in InP-wafers
A III-V wafer was grown and bonded to Si
Silver encapsulation
Periodic report (M1-M18)
Nanopillar on waveguide
Ohmic contacts
SiOx
Reported in MS10

## Slide 14: Plasmonic Modulator Approaches
Reported in MS9 & D3.2
SPP absorption modulator
SPP phase modulator

## Slide 15: Task 3.2 Modelling of the Modulator
Upp=4.5V
Large figure of merit
Easy coupling structure
Easier fabrication
SPP phase modulator

## Slide 16
Task 3.4 Fabrication of the Modulator
A. Melikyan, et al. "Surface Plasmon Polariton High-Speed Modulator," in CLEO: 2013, PDP paper CTh5D.2
Passive silicon-on-insulator (SOI) wafer processing
E-beam lithography for defining 140 nm wide slot in gold
Coating with an electro-optic polymer
Poling of electro-optic polymer with static electric field
Reported in MS11

## Slide 17
Vm = 0.8 V
r33 ≈ 21 pm / V
VpL = 1.3 Vmm
Vm = 0.1 V
A. Melikyan, et al. "Surface Plasmon Polariton High-Speed Modulator," in CLEO: 2013, PDP paper CTh5D.2
Task 3.4 Fabrication of the Modulator
65 GHz RF bandwidth (lc = 1.55mm)
Broadband optical operation (fm = 45GHz)
Characterization results

## Slide 18
Upp = 4.9V
BER = 6 × 10-5
Task 3.4 Fabrication of the Modulator
Demonstration ‒ DPSK Data Modulation
Electrical signal (40Gbit/s)
Optical signal (40Gbit/s)

## Slide 19: Summary and Outlook
  Summary
    Metal-cavity lasers and plasmonic modulators were simulated
    Lithographic and etching processes to fabricate the nanolaser were developed. Fabrication tests were done
    Growth of III-V wafer and bonding to Si for the fabrication of nanolaser
    Plasmonic phase modulator has been successfully demonstrated
Bandwidth > 65 GHz
Broadband optical operation: Dl > 120 nm
VpL = 1.3 Vmm for r33 ≈ 21 pm / V
Length: 29 mm
Insertion loss (incl. transitions): 14 dB
  Outlook
    Fabrication of nanolaser in wafer with real layer stack
    Improvement of plasmonic phase modulator fabrication
    Fabrication and testing of SPP absorption modulator