## Slide 1
Work Package 5 Presentation
Dries Van Thourhout
IMEC, Belgium

## Slide 2: WP5 Position in Project
Contributors:

## Slide 3: Objectives
Overall Objective :
Specific Objectives:
  Coupling light between silicon backbone and plasmonic devices
  Beam Shaping grating couplers to direct light between chips
  Compact filters for noise suppression
  Specify and implement Dual Die Communication Module (DDCM)
Design and implement optical and electrical interfaces for plasmonic interconnect

## Slide 4: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24

## Slide 5: Milestones
 | Names of the Milestones | Month | Partner
MS25 | Decision on optimized plasmonic waveguide couplers | 6 | KIT
MS26 | Fabrication of plasmonic waveguide couplers with less than 3 dB coupling loss | 12 | KIT
MS27 | Design of first generation beam shapers and compact optical filters | 12 | IMEC
MS28 | DDCM with electrical PHY design and verification | 12 | ST
MS29 | Data codecs for power consumption reduction | 15 | ST
MS30 | Decision on plasmonic waveguide couplers with less than 3 dB coupling loss | 15 | KIT
MS32 | Fabrication of compact optical filters and first generation beam shapers | 18 | IMEC
MS33 | Data codecs for error detection and correction | 18 | ST

## Slide 6: Milestones
 | Names of the Milestones | Month | Partner
MS33 | Design of second generation beam shapers | 24 | imec
MS34 | Generic DDCM compatible with plasmonic-based PHY | 24 | ST
MS35 | Fabrication of second generation beam shapers | 39 | imec
MS36 | DDCM evolution for NiP solutions | 39 | ST

## Slide 7: Deliverables
 | Names of the Milestones | Month | Partner
D5.1 | DDCM specification document | 6 | ST
D5.2 | DDCM with electrical PHY design and verification data base | 12 | ST
D5.3 | Compact optical filters (2nm bandwidth, >30nm FSR) and first generation beam shapers | 21 | imec
D5.4 | Generic DDCM compatible with plasmonic-based PHY specification document | 24 | ST
D5.5 | Report on plasmonic waveguide couplers | 24 | imec
D5.6 | Generic DDCM compatible with plasmonic-based PHY design and verification data base | 39 | st
D5.7 | Second generation beam shapers (distance 1mm, with bandwidth > 10nm and efficiency > 3dB) | 39 | imec

## Slide 8: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24

## Slide 9: Task 5.1 Modeling and Fabrication of SPP Couplers
q
Finite Difference Time Domain (FDTD) method is used
Couplers are optimized for their highest transmission
Reported in MS25 (month 6)

## Slide 10: Task 5.1 Modeling and Fabrication of SPP Couplers
Broadband taper coupling
Deviced fabricated for loss estimation

## Slide 11: Task 5.1 Modeling and Fabrication of SPP Couplers
Photonic-to-plasmonic mode converter
A. Melikyan et al., Opt. Lett. 39, (2014)
Glass cladding
Electro-optic material cladding
g=30nm
g=60nm

## Slide 12: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24

## Slide 13: Task 5.2 – Optical Beam Steerers
Global idea: Couple light between two chips by vertical grating couplers
First generation (completed month 18):
Demonstrated electrostatically movable gratings to facilitate alignment
Second generation: Develop focusing grating coupler
  Need larger grating  lower index contrast
  Hence: combine standard ePIXfab platform with eBEAM for grating
  Status:
  Efficiency trade-offs evaluated
  ePIXfab design submitted and in fabrication
  Target for finalization: month 39

## Slide 14: Task 5.2 – Optical Beam Steerers
Chart: Distance between chips [um]
| 10.0 | 30.0 | 100.0 | 300.0 | 700.0 | 1000.0
Grating = 4um | 15.8789 | 38.3309 | 123.7498 | 370.1703 | 863.4735 | 1233.4913
Grating = 8um | 20.9293 | 27.2455 | 64.8344 | 186.0955 | 432.1708 | 617.0496
Grating = 12um | 30.2804 | 32.4367 | 50.8964 | 126.941 | 289.3645 | 412.2433
Grating = 16um | 40.1187 | 41.0558 | 50.5062 | 100.7863 | 219.5288 | 310.9462
Grating = 20um | 50.0608 | 50.5447 | 55.7545 | 89.3143 | 179.7761 | 251.7062
Grating = 24um | 60.0352 | 60.3161 | 63.4241 | 86.0436 | 155.9101 | 214.1521
Grating = 28um | 70.0222 | 70.1993 | 72.1837 | 87.7178 | 141.8239 | 189.6022
Grating = 32um | 80.0149 | 80.1336 | 81.4722 | 92.4093 | 134.3437 | 173.7006
Grating = 36um | 90.0104 | 90.0939 | 91.0375 | 98.9467 | 131.5429 | 163.9595
Grating = 40um | 100.0076 | 100.0684 | 100.7578 | 106.6267 | 132.1169 | 158.7892
Optimum | 15.8789 | 27.2455 | 50.5062 | 86.0436 | 131.5429 | 158.7892
Chart: Distance between chips [um]
| 10.0 | 30.0 | 100.0 | 300.0 | 700.0 | 1000.0
Grating = 4um | 11.7488 | 21.0313 | 62.478 | 185.2877 | 431.8236 | 616.8065
Grating = 8um | 20.2363 | 22.0359 | 36.7543 | 94.6461 | 216.7785 | 309.0106
Grating = 12um | 30.0704 | 30.6274 | 36.3677 | 68.5821 | 146.9965 | 207.7526
Grating = 16um | 40.0297 | 40.2665 | 42.8686 | 61.1512 | 115.1009 | 159.2856
Grating = 20um | 50.0152 | 50.1367 | 51.4989 | 62.2034 | 99.7741 | 133.094
Grating = 24um | 60.0088 | 60.0792 | 60.8741 | 67.4602 | 93.6856 | 119.018
Grating = 28um | 70.0055 | 70.0499 | 70.5523 | 74.8238 | 93.2926 | 112.5267
Grating = 32um | 80.0037 | 80.0334 | 80.3706 | 83.2759 | 96.499 | 111.0989
Grating = 36um | 90.0026 | 90.0235 | 90.2605 | 92.318 | 101.9847 | 113.118
Grating = 40um | 100.0019 | 100.0171 | 100.19 | 101.6972 | 108.9207 | 117.4883
Optimum | 11.7488 | 21.0313 | 36.3677 | 61.1512 | 93.2926 | 111.0989
optimum
optimum
a) Standard grating
b) Focussing grating

## Slide 15: Task 5.2 – Optical Beam Steerers
Status
  Mask completed, designs under fabrication
Applications ?
  Free space chip-chip coupling no longer considered in project
  Also no longer considered in industry as a whole
  Still useful in some dedicated applications
    Coupling to VCSEL above grating coupler
    Transmission between levels in 3D-integrated chip modules
Design under fabrication

## Slide 16: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24
Completed according to spec month 18

## Slide 17: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24
Completed according to spec month 18

## Slide 18: Task 5.4 – Signal Generation Module Design
DDCM Tx
DDCM Rx
Die #1
Die #2
STNoC/STBus/AXI initiator
Virtual wires
Virtual wires
Request traffic flow
Response traffic flow
Virtual wires
Unidirectional physical links
DDCM Tx
DDCM Rx
STNoC/STBus/AXI target
STNoC/STBus/AXI initiator
STNoC/STBus/AXI target
A DDCM consists of a transmitter (DDCM Tx) and a receiver (DDCM Rx)
The DDCM is a parametric design that can be configured properly in order to meet specific system requirements and needs in terms of interfaces, FIFOs sizes, clock domains synchronization and functionality
A VHDL model of the plasmonics-based PHY has been developed in order to be co-simulated with the digital parts

## Slide 19: Tasks
 | Names of the Tasks | Time Period [months]
Task 5.1 | Modeling and fabrication of coupling Si waveguide to plasmonic waveguide | 1 – 15
Task 5.2 | Design and fabrication of Si beamshaper | 1 – 30
Task 5.3 | Design and fabrication of passive ultra-compact components as filters | 1 – 15
Task 5.4 | Signal generation module design | 4 – 12
Task 5.5 | Signal Generation Module implementation via FPGA | 13 – 24

## Slide 20: Task 5.4 – Signal Generation Module Implementation via FPGA
After digital design and functional verification phases, the developed VHDL code has been synthesized in order to get a gate level netlist of the DDCM
The synthesis environment is fully based on Synopsys tools
The technologies used for synthesis were CMOS 65nm and 40nm from ST
A flow for the characterization of the digital parts of the DDCM in terms of power consumption has been developed as well
The synthesis flow for FPGA has been carried out with the ZeBu equipment in ST
The synthesis engine in this case translates the VHDL design into a set of logic structures that can be mapped into the hardware basic logic structures available in the ZeBu FPGA chip.
The FPGA chip has been verified with the same environment used for VHDL

## Slide 21: Summary
WP5 largely completed
Optical interfaces designed, fabricated and tested
  Coupler dielectric <> plasmonic waveguide
  Optical filters
  Optical beam shapers
Electrical interfaces designed and implemented

## Slide 22: Outlook
Task 5.1 – Couplers
  Completed (month 24)
Task 5.2 – Beam shapers
  Finalizing second generation fabrication
Task 5.3 – Filters
  Completed (month 18)
Task 5.4 – Signal generation module design
  Completed (month 18)
Task 5.5 – DDCM FPGA implementation
  Completed (month 36)